## Slide 1: Air-Synth ProjeT Geste et Intelligence Artificielle
Xiangnan, Xu
Tuteur : Edgar

## Slide 2: Table of Content
Introduction
Tools
  Leap Motion
  Ableton Live
Introduction Midi
Music Stream
Gesture recognition
Algorithm
Conclusion

## Slide 3: Introduction
Create music from gesture.
Control the sounds notation and octave.

## Slide 4: Leap Motion

## Slide 5: Ableton Live

## Slide 6: Midi
Musical Instrument Digital Interface
Key parameter:
  Notation
  Pitch
  Velocity
Python library: python-rtmidi 1.1.0
  Usage example: note_on = [0x90, 60, 112] note_off = [0x80, 60, 0] midiout.send_message(note_on) time.sleep(0.5) midiout.send_message(note_off)

## Slide 7: Music Stream
Leap Motion
API Python
Create midi stream
virtual port
Ableton Live

## Slide 8: Gesture recognition
Chart: Y-axis changes with frames

## Slide 9: Finger Moving
Simulation : play the piano in the air
Condition:
  The velocity of fingertip changes direction
  Distance from leap motion < h = 6cm
  Distance of fingertip to palm center reduces
  Position change of fingertip is large enough
Parameters sent to midi stream
  Velocity: velocity of fingertip
  Time of a note: one frame( about 0.05 s)

## Slide 10: Notation Distribution
'left4':'C', 'left3':'D', 'left2':'E', 'left1':'F', 'left0':'F#', 'right0':'G', 'right1':'G#', 'right2':'A', 'right3':'A#', 'right4':'B'

## Slide 11: Octave Distribution
Leap Motion

## Slide 12: Conclusion
Live Demostration
To be improved:
  Distinguish the initiative movement and passive movement of fingers
    Thumb moving conditions different from others
    Ring Finger and Pinky Finger Move together
  Sensitivity difference between left and right hand, and among different users
  Find the best threshold parameters (distance, velocity)
  Use different criteria as the Leap Motion is sometimes insensitive

## Slide 13: Thanks QUESTIONs?